## Slide 1: Stay healthy, free flu shots for students!
Full schedule and details here
Thursday, October 27 | 6:30 a.m. to 4:30 p.m. | University Services Building
Tuesday, November 1 | 8.30 a.m. to 11:30 a.m. and 1 p.m. to 4 p.m. | Buchanan D140, Meekison Lounge
Wednesday, November 2 | 8.30 a.m. to 11:30 a.m. and 1 p.m. to 4 p.m. | The Nest
Thursday, November 3 | 8.30 a.m. to 11:30 a.m. and 1 p.m. to 4 p.m. | The Nest

## Slide 2
Quiz 1, P3 - A system contains carbon dioxide and water under vapour-liquid equilibrium and there are no chemical reactions involved. How many degrees of freedom does the system have?
~ 63% correct
DF = 2 + c – Π – r
= 2 + 2 components (CO2, H2O) – 2 phases (V-L) – 0 reactions = 2 DF

## Slide 3
Quiz 1, P4 – What is the dew point temperature in Celsius for benzene at 5.24 psia?
~ 20% correct Multiple methods to solve
NIST – 49.98 (Note +/- 2 C was also accepted)
Antoine Equation - Data from NIST Webbook, also in text Table B4

## Slide 4: Practice Problems
Tutorial videos sponsored by UC Boulder and Shell
Online – organized same as the text we use
http://www.learncheme.com/screencasts/mass-energy-balances

## Slide 5: Adsorption

## Slide 6: Adsorption on solids
Adsorption – molecules of gas, liquid or solid, called the adsorbate, adhere to a solid surface, called the adsorbent
Absorption – molecules of gas, liquid or solid dissolve into another substance known as the absorbent for solids or solvent for liquids
Adsorption Equilibrium data is taken at a particular temperature and known as an adsorption isotherm

## Slide 7
P CCl4 (mmHg) | 0 | 0.169 | 3.38 | 6.76 | 8.45 | 11.8 | 20.7 | 32.1 | 40.0 | 84.5 | 104.5 | 123 | 133
X* (g CCl4/g carbon) | 0 | 0.07 | 0.14 | 0.27 | 0.34 | 0.48 | 0.57 | 0.63 | 0.68 | 0.70 | 0.71 | 0.71 | 0.71
Table 6.7-1 Equilibrium data for CCl4 adsorbed on activated carbon at 34°C

## Slide 8
P CCl4 (mmHg) | 0 | 0.169 | 3.38 | 6.76 | 8.45 | 11.8 | 20.7 | 32.1 | 40.0 | 84.5 | 104.5 | 123 | 133
X* (g CCl4/g carbon) | 0 | 0.07 | 0.14 | 0.27 | 0.34 | 0.48 | 0.57 | 0.63 | 0.68 | 0.70 | 0.71 | 0.71 | 0.71
Chart: P CCl4 (mmHg)
| 0 | 1.69 | 3.38 | 6.76 | 8.4499999999999993 | 11.8 | 20.7 | 32.1 | 40 | 84.5 | 104 | 123 | 133
X* (g CCl4/g carbon) | 0 | 0.07 | 0.14 | 0.27 | 0.34 | 0.48 | 0.57 | 0.63 | 0.68 | 0.7 | 0.71 | 0.71 | 0.71
Table 6.7-1 Equilibrium data for CCl4 adsorbed on activated carbon at 34°C

## Slide 9
P CCl4 (mmHg) | 0 | 0.169 | 3.38 | 6.76 | 8.45 | 11.8 | 20.7 | 32.1 | 40.0 | 84.5 | 104.5 | 123 | 133
X* (g CCl4/g carbon) | 0 | 0.07 | 0.14 | 0.27 | 0.34 | 0.48 | 0.57 | 0.63 | 0.68 | 0.70 | 0.71 | 0.71 | 0.71
Chart: P CCl4 (mmHg)
| 0 | 1.69 | 3.38 | 6.76 | 8.4499999999999993 | 11.8 | 20.7 | 32.1 | 40 | 84.5 | 104 | 123 | 133
X* (g CCl4/g carbon) | 0 | 0.07 | 0.14 | 0.27 | 0.34 | 0.48 | 0.57 | 0.63 | 0.68 | 0.7 | 0.71 | 0.71 | 0.71
Linear region
or
K is fitted to data
Table 6.7-1 Equilibrium data for CCl4 adsorbed on activated carbon at 34°C

## Slide 10
Chart: P CCl4 (mmHg)
| 0 | 1.69 | 3.38 | 6.76 | 8.4499999999999993 | 11.8 | 20.7 | 32.1 | 40 | 84.5 | 104 | 123 | 133
X* (g CCl4/g carbon) | 0 | 0.07 | 0.14 | 0.27 | 0.34 | 0.48 | 0.57 | 0.63 | 0.68 | 0.7 | 0.71 | 0.71 | 0.71
P CCl4 (mmHg) | 0 | 0.169 | 3.38 | 6.76 | 8.45 | 11.8 | 20.7 | 32.1 | 40.0 | 84.5 | 104.5 | 123 | 133
X* (g CCl4/g carbon) | 0 | 0.07 | 0.14 | 0.27 | 0.34 | 0.48 | 0.57 | 0.63 | 0.68 | 0.70 | 0.71 | 0.71 | 0.71
Linear region
or
K is fitted to data
Langmuir Isotherm
or
a, KL is fitted to data
Table 6.7-1 Equilibrium data for CCl4 adsorbed on activated carbon at 34°C

## Slide 11
Chart: P CCl4 (mmHg)
| 0 | 1.69 | 3.38 | 6.76 | 8.4499999999999993 | 11.8 | 20.7 | 32.1 | 40 | 84.5 | 104 | 123 | 133
X* (g CCl4/g carbon) | 0 | 0.07 | 0.14 | 0.27 | 0.34 | 0.48 | 0.57 | 0.63 | 0.68 | 0.7 | 0.71 | 0.71 | 0.71
X* line | 0 | 0.1108 | 0.19446 | 0.31239 | 0.3555 | 0.42159 | 0.52803 | 0.59928 | 0.62975 | 0.70664 | 0.72149 | 0.73178 | 0.7361
P CCl4 (mmHg) | 0 | 0.169 | 3.38 | 6.76 | 8.45 | 11.8 | 20.7 | 32.1 | 40.0 | 84.5 | 104.5 | 123 | 133
X* (g CCl4/g carbon) | 0 | 0.07 | 0.14 | 0.27 | 0.34 | 0.48 | 0.57 | 0.63 | 0.68 | 0.70 | 0.71 | 0.71 | 0.71
Linear region
or
K is fitted to data
Langmuir Isotherm
or
a, KL is fitted to data
a = 0.794 g CCl4/g carbon
KL = 0.096 (mmHg)-1
Table 6.7-1 Equilibrium data for CCl4 adsorbed on activated carbon at 34°C

## Slide 12
Ex 6.7-1 from text: A 50.0 L tank contains an air-carbon tetrachloride mixture at 1 atm absolute, 34°C, and 30.0% relative saturation. Activated carbon is placed in the tank to absorb CCl4. The tank pressure is maintained at 1.00 atm by feeding in pure air and the temperature is kept at 34°C.
Calculate the minimum amount of activated carbon needed to reduce the CCl4 mole fraction in the gas to 0.001. Neglect the volume of activated carbon and the absorbed CCl4.
Working backwards, what is the strategy to solve this problem?
Question text: Elementary Principles of Chemical Processes, 4/E by Richard M. Felder, Ronald W. Rousseau, and Lisa G. Bullard Copyright © 2016 by John Wiley & Sons, Inc.
V=50 L
T=34°C
P=1atm
Carbon
V=50 L
T=34°C
P=1atm
Carbon + CCl4

## Slide 13
Ex 6.7-1 from text: A 50.0 L tank contains an air-carbon tetrachloride mixture at 1 atm absolute, 34°C, and 30.0% relative saturation. Activated carbon is placed in the tank to absorb CCl4. The tank pressure is maintained at 1.00 atm by feeding in pure air and the temperature is kept at 34°C.
Calculate the minimum amount of activated carbon needed to reduce the CCl4 mole fraction in the gas to 0.001. Neglect the volume of activated carbon and the absorbed CCl4.
Question text: Elementary Principles of Chemical Processes, 4/E by Richard M. Felder, Ronald W. Rousseau, and Lisa G. Bullard Copyright © 2016 by John Wiley & Sons, Inc.
V=50 L
T=34°C
P=1atm
a = 0.794 g CCl4/g carbon
KL = 0.096 (mmHg)-1
Carbon
V=50 L
T=34°C
P=1atm
Carbon + CCl4
Relative Saturation

## Slide 14: Summary
Intro to phase diagrams

## Slide 15: Summary
Intro to phase diagrams
Species vapour pressure and boiling point
Gibb’s phase rule: DF = 2 + c – Π – r
Raoult’s Law:
Henry’ Law:
Solubility
Colligative properties – boiling point elevation, melting point depression
Liquid extraction
Adsorption - isotherms

## Slide 16: Summary
Intro to phase diagrams
Species vapour pressure and boiling point
Gibb’s phase rule: DF = 2 + c – Π – r
Raoult’s Law:
Henry’ Law:
Solubility
Colligative properties – boiling point elevation, melting point depression
Liquid extraction
Adsorption - isotherms
Image: By Power.corrupts (Own work) CC BY-SA 3.0 via Wikimedia Commons

## Slide 17: End of Content covered by midterm 2

## Slide 18: Energy Balances
Image: By Siemens (Siemens website) CC-BY-SA-3.0 via Wikimedia Commons

## Slide 19: Learning objectives
By the end of this class you will be able to:
Identify relevant terms for energy balances for open and closed systems
Calculate changes in various forms of energy for a system
Content is Ch 7-7.4

## Slide 20: Forms of Energy
Kinetic - - Translational or rotational energy
or is for flowing systems
[=] mass
[=] velocity relative to a reference (generally earth’s surface)

## Slide 21: Forms of Energy
Kinetic - - Translational or rotational energy
or is for flowing systems
Potential - - Energy due to position in a field such as gravitational or magnetic
or
[=] mass
[=] gravitational acceleration (~9.8 m/s2 on earth’s surface)
[=] height above a reference

## Slide 22: Forms of Energy
Kinetic - - Translational or rotational energy
or is for flowing systems
Potential - - Energy due to position in a field such as gravitational or magnetic
or
Internal - - All other energy in a system, e.g. motion and interaction of molecular, atomic and sub-atomic particles

## Slide 23: Energy transfer in closed systems
Closed System – No mass transfer across system boundaries
Heat - – Energy flow due to temperature difference.
– Direction of flow is always from higher to lower temperature
– Positive when transferred to the system from the surroundings
Work - W – Energy flow as a response to a driving force other than temperature (e.g. force, torque, voltage)
– Text defines as positive when transferred to the system from the surroundings, I will use this, however, it can be the opposite.

## Slide 24: Energy balances on closed systems
Law of conservation of energy (we assume no nuclear reactions)
Accumulation = Input - Output
final system E – initial system E = net E transferred to the system (in-out)
initial energy:
final energy:
energy transferred:

## Slide 25
First Law of thermodynamics - change in the internal energy of a closed system is equal to the amount of heat supplied to the system, minus the amount of work done by the system on its surroundings.
Important notes
Internal energy depends on chemical composition, state (solid, liquid, gas) and temperature of a system. Pressure has little effect.
No acceleration , no change in height
Same T as surroundings or perfectly insulated, adiabatic, Q = 0
No moving parts, electrical currents, radiation at system boundary, W = 0

## Slide 26: Work in Open Systems
Open System – Mass crosses system boundaries (along with energy)
We typically define 2 types of work in these systems
Shaft work - or - Work done on process fluid by a moving part (eg. pump)
Flow work - or - Work done on process fluid at inlet minus outlet
Process Unit
(m3/s)
(N/m2)
(m3/s)
(N/m2)

## Slide 27: Specific properties
Specific property - – intensive property obtained by dividing extensive property by a total amount (or flow rate)
or

## Slide 28: Steady-state open-system energy balance
How do we get to:

## Slide 29
Ex 7.4-2 from text
Five hundred kilograms per hour of steam drives a turbine at 44 atm and 450°C at a linear velocity of 60 m/s and leaves at a point 5 m below the turbine inlet at atmospheric pressure and a linear velocity of 360 m/s. The turbine drives a motor producing 70 kW and has a heat loss of roughly 104 kcal/h. Calculate the specific enthalpy change based on this process
Question text: Elementary Principles of Chemical Processes, 4/E by Richard M. Felder, Ronald W. Rousseau, and Lisa G. Bullard Copyright © 2016 by John Wiley & Sons, Inc.